## Slide 1: Supervisor: Professor Essam Shehab Co-Supervisor: Professor Md. Hazrat Ali Nursultan JYENISKHAN 2nd Year Master in Mechanical & Aerospace Engineering
Investigation of Developing Digital Twin for Additive Manufacturing
2023
Notes: Presentation time 25 min.

## Slide 2: Outline
2
Introduction
Background Information
Research Motivation
Research Scope
Aim & Objectives
Research Gap Analysis
Methodology
Recent Developments
Results
DT Framework & Architecture
Workflow of Proposed System
Hardware & Software
Design Implementations & Layout
Discussion
Conclusion & Future Work Areas
Key Research Contribution to Knowledge

## Slide 3: Introduction
3
Additive Manufacturing (AM)
Layer-by-layer
Demand for customized product
Complex/non-standard components
(Pant et al., 2021)
Digital Twin (DT)
Digital replica
Gradual development
Expected solutions for AMs
Real-time monitoring & controlling
Predicting process fault
(Zhang et al., 2020)
4.0

## Slide 4: Background Information
4
Digital Model (a), Digital Shadow (b), Digital Twin (c) (Khandare et al., 2022)

## Slide 5: Research Motivation
5
Illustrations of the seven categories of 3DP processes
(Dave & Patel, 2021)
Part defects
Real-time monitoring
Predictive errors
Process optimization
Cost, time, material waste
Overwhelming to control and monitor all printing processes by human

## Slide 6: Research Scope
6
Cost Modeling
AM Applications
Maintenance
Supply chain
Traditional Manufacturing
FDM 3D Printer
DTs for FDM Printer
Framework / Models
DT Functions
AM: Additive Manufacturing
DT: Digital Twin

## Slide 7: Research Gap Analysis
7
Literature Review
Additive Manufacturing
Digital Twin
DT for AM
FDM
DT Modeling
Recent Developments
Process Parameters & Defects
Research Gap Analysis
Limited functionality of digital twin (DT) models
Lack of universal DT architecture
DT Implementation challenges

## Slide 8: Aim & Objectives
8
Developing a Digital Twin (DT) for Fused Deposition Modeling (FDM) 3D Printers
Objectives
Identify printing process parameters & their effects on final products / defects
Develop digital twin Framework & Architecture for FDM printer
Create digital twin for FDM printer
Validate the digital twin model

## Slide 9: Methodology
9

## Slide 10: Recent Developments
10
The 3D printer and its stateful digital twin in Unity Engine
(Pantelidakis et al., 2022)
● Odada et al. (2021), and Pantelidakis et al. (2022) – Data driven Digital Twin

## Slide 11: Recent Developments
11
Test bench
(Stavropoulos et al., 2021)
Data visualization
Same with previous, but using different equipment
Stavropoulos et al. (2021)

## Slide 12
Results: DT Framework
12
ML: Machine Learning

## Slide 13
Results: DT Architectural Design
13

## Slide 14: Results: DT Workflow of FDM
14
Remotely controlling the FDM printer via open-source software
Extract all data from one place
Store the extracted data in database
Processing the extracted data via machine learning model
Monitor & control all processes in one place (Augmented Reality (AR) platform)
Note: DT Functional Requirements
Control & Monitor Remotely
Communicate P-V & V-P
Integrate intelligence

## Slide 15: Hardware & Software
15
FDM printer (InterPrint)
Raspberry Pi3B+
Chair Lamp
Logitech web camera
Octoprint open source software
Database
Python for Machine Learning
Unity Client

## Slide 16: Implementation
16

## Slide 17: Implementation
17
Installing OctoPi to Raspberry Pi
Connecting Raspberry Pi to Printer
Remotely monitor and control the InterPrint through Octoprint
Installing extra sensors
Extracting data from Octoprint
Store data in database
Process data with Machine learning model
Send info to Unity
Use real-time data in Unity to show printing status and other information
Use unity to remotely monitor & control the FDM printer through Octoprint
1
2
1
1
1
2

## Slide 18: Results: OctoPrint Interface
Real-time printing status
Nozzle & bed temperature
Real-time temperature data visualization
Note: Data extraction of printing status & temperatures
18

## Slide 19: Results: OctoPrint Interface
19
Real-time monitoring through web camera
Remotely control the nozzle through XYZ axis
Remotely control the nozzle feed and extrusion flow rate
Note: Real-time remote monitoring & controlling through the Octoprint

## Slide 20: Results: OctoPrint Interface
20
Gcode viewer tab
Real-time extrusion footprint
Note: Data extraction of the nozzle movement

## Slide 21: Results: Real-time Temperature
21

## Slide 22: Results: Unity Client (Nozzle & Bed)
22

## Slide 23: Results: Unity Interface
23

## Slide 24: Results: Data Flow (P-V)
Connecting Pi to the FDM
Remotely connection to the Printer through Pi
Real-time video processing by machine learning model
All-in-one platform and visualization
24
From Physical to Virtual World (P-V)

## Slide 25: Results: Data Flow (V-P)
Send command to the Printer through Octoprint
Send received commands to FDM printer through Pi
Executing command in physical world
25
If any Defect detection by machine learning model
From Virtual to Physical World (V-P)

## Slide 26: Discussion
26
  Meets its functional requirements
Strengths
  Receive data from in-built sensors
  Less equipment & Less complex
  Data flow is quicker (External factor is Wifi speed)
  Available for upgrades
Note: Careful with computational burden and Interoperability when upgrading model

## Slide 27: Limitations & Recommendations
27
Limitations
  Local network connection
  Limited intelligence
  Optimization of printing parameters
Recommendations (Immediate future)
  Wide network connection
  Database (Local)
  Machine learning model for complex geometries

## Slide 28: Conclusion
28
  Recent Developments in digital twin for FDM 3D printers
  Constructed digital twin framework & architecture for FDM printers
  Experimental setup
  Established connection between digital and physical models
  Integration of machine learning model
  Unity client was developed for user friendly interface
  Unity client holds all components of digital twin in one platform

## Slide 29: Future Research Areas
29
  Universally accepted DT Framework, architecture, & model for all types of AMs
  Extended Reality for user-friendly experience
  Achieving closed-loop effective digital twin model
  Artificial intelligence for all defects
  Fully-automatic DT model for AMs
  Integration of AI-integrated machine health monitoring system
  Reality Gap
AM: Additive Manufacturing
DT: Digital Twin

## Slide 30: Key Research Contributions
30
  Identification of digital twin implementation benefits in different levels
  Identification of digital twin implementation challenges
  Digital twin framework & architecture for FDM printers
  Acquisition of bidirectional communication between models
  Novel digital twin model with some level of intelligence
  Real-time monitoring & controlling

## Slide 32
References
32
Dave H. K., & Patel, S. T. (2021). Introduction to fused deposition modeling based 3D printing process. Springer International Publishing, doi: 10.1007/978-3-030-68024-4_1.
Khandare, A. D., Jadhav, V. ., Deshmukh, S. P., & Rane, K. K. (2022). Digital twins for manufacturing process and system: a state of the art review’, ECS Trans, 107(1), pp. 15497–15508, doi: 10.1149/10701.15497ecst.
Odada, C.A., Byiringiro, J. B., & Madaraka, F. M. (2021). Development of data-driven digital twin for real-time monitoring of FDM 3D printer. J. Mech. Eng. Autom., 2021(2), pp. 25–35,
Pant, M., Pidge, P., Nagdeve, L., & Kumar, H. (2020). A review of additive manufacturing in aerospace application. Journal of Composite and Advanced Materials, 31(2), pp. 109–115, 2020, doi: 10.18280/rcma.310206.
Pantelidakis, K. Mykoniatis, J. & Harris, G. (2022). A digital twin ecosystem for additive manufacturing using a real-time development platform,” Int. J. Adv. Manuf. Technol., 120,(9–10), pp. 6547–6563,
Stavropoulos, P., Papacharalampoloulos, A., & Tzimanis, K. (2021). Design and Implementation of a digital twin platform for AM processes. Procedia CIRP, 104, 1722–1727. https://doi.org/10.1016/j.procir.2021.11.290
Zhang, L., Chen, X., Zhou, W., Cheng, T., Chen, L., Guo, Z., Han, B., & Lu, L. (2020). Digital twins for additive manufacturing: A state‐of‐the‐art review. Applied Sciences (Switzerland), 10(23), 1–10. https://doi.org/10.3390/app10238350