## Slide 1: Baqsh’Astana Interiority as a sustainable strategy
LAMBOTTE Sophie / LI Xiang
FRANCE ENSA-PARIS MALAQUAIS

## Slide 2: Design concept

## Slide 3
DIVISION
of the program’s volume in 12 buildings
OPTIMISATION
of views from the dwellings, solar orientation and reduction of wind’s speed

## Slide 4
PATIOS
as intimate and protected collective spaces for the inhabitants
DIG
ground’s depth to install patios and car park space

## Slide 5
PRIVATE AND SEMI-PRIVATE CIRCULATION
through horizontal and vertical smaller distribution systems
PUBLIC CIRCULATION
along two major axis

## Slide 6
DIFFERENT SHADES OF SPACE
from public to private, from outside to inside
STIMULATION
of the public space thanks to public amenities along the public way

## Slide 7
Housing
12 buildings
322 dwellings (from T2 to T4)
Ground surface area : 3900 sqm
Total gross floor area : 30116 sqm
Public amenities
Public bath : 1200 sqm Retail shops : 665 sqm Restaurant : 580 sqm Total gross floor area : 1555 sqm
Patios
Botanic greenhouses
Vegetable garden greenhouses Children playgrounds
Green space areas
Parking
400 car park spaces 5000 sqm
A vertically stacked program
Density
Total ground surface built area : 5500 sqm
Ratio : 0.18
Level
+1 to +8
Level 0
Level -1
Level -1

## Slide 8: Architectural design Site implantation

## Slide 9: Basement floor plan
Parking access
Parking access
PARKING

## Slide 10: PARKING
BUIDING’S FOOTPRINT
Basement floor plan

## Slide 11: PARKING
Basement floor plan
BUIDING’S FOOTPRINT
PUBLIC AMENITIES

## Slide 12: PARKING
Basement floor plan
BUIDING’S FOOTPRINT
PUBLIC AMENITIES PATIOS

## Slide 13
View from a patio

## Slide 14: Ground floor plan

## Slide 15: BUILDING’S FOOTPRINT
Ground floor plan

## Slide 16: BUILDING’S FOOTPRINT
Ground floor plan
PUBLIC AMENITIES

## Slide 17: BUILDING’S FOOTPRINT
Ground floor plan
PUBLIC AMENITIES
CIRCULATION

## Slide 18
View from a lane

## Slide 19: Common floor plan

## Slide 20: TYPE A
Common floor plan
TYPE B
TYPE C

## Slide 21
View from a dwelling

## Slide 22
A
B
A
B
A Cross section
B Longitudinal section

## Slide 23: Architectural design The building

## Slide 24: building shell
N
S
Composition of the
Different layers according to the orientation
Opaque and high insulated wall with triple-glazing win-
dows
Glazing area : 99 sqm
Sliding wooden sun louvers
Built-in furnishing
Triple glazing bay windows Glazing area : 295 sqm
Total glazing area : 460 sqm
Daylight autonomy : 67 %
Opaque concrete wall with vertical triple-glazing windows
Glazing area : 33 sqm
Perforated steel sun louvers

## Slide 25: Axonometry of a dwelling
Common floor plan for building type A

## Slide 26: CENTRAL BLOCK
Common floor plan for building type A
Axonometry of a dwelling

## Slide 27: DAY / SOUTH
Common floor plan for building type A
Axonometry of a dwelling
NIGHT / NORTH

## Slide 28
View from the living room

## Slide 29
View from the bedroom

## Slide 30: Technical strategies

## Slide 31
Overall sustainable strategies
Dual flow ventilation
with heat recovery and by/pass system for summer
Heat recovery system : 95 % Airflow ventilation rate : 300 mc per hour to reach a low level of CO2 concentration
North facade
High insulated for minimal heat loss
South facade
Porosity to maximise natural sunlight and sun’s
heating energy
Rainwater collection
Re-use of grey water,
including rainwater for watering gardens and green-
houses
Use of photovoltaïc
solar panels
as a supplementar source of
electricity

## Slide 32: Thermal strategies
Low heat conductiviy of building components
A / ISOVER Sillatherm WVP 1-035
λ = 0, 036 W / mK
High thermal capacity of building components
Concrete structure
Heat capacity = 2500 Kj / m2K
WINTER
SUMMER
Airtightness of 0.6 V/h guaranteed by impermability of ISOVER VARIO KM
Duplex membrane
Airtightness of 0.6 V/h guaranteed
by permability of
ISOVER VARIO KM
Duplex membrane
DUAL FLOW VENTILATION
integrated into the central technical block
NATURAL CROSS VENTILATION
using south-west wind speed
PASSIVE HEATING
by solar gains
PASSIVE COOLING
by wooden sun louvers
B
A
B / ISOVER Akustic EP 3040 / TP1
λ = 0, 04 W / mK

## Slide 33: Acoustic strategies
Vegetation as a buffer screen for external noises
High performing sound insulation building components
A / ISOVER Akustic TP1 R = 25 db
B / ISOVER Akustic HWP 1 R = 79 dB
C / Concrete structure R= 70 dB
D / ISOVER Sillatherm WVP 1-035 R = 23 dB
E / ISOVER Gaineo R = 26 dB
Outdoor environment
30 dB(tr)
Dwelling unit
60 dB(tr)
HVAC Ducts
50 dB(tr)
D
A
E
C
B

## Slide 34: Fire security strategies
Euroclasse values for building components Euroclasse A1 / M0 : non-combustible
Evacuation path
A / ISOVER Sillatherm WVP 1-035
B / ISOVER AKUSTIC EP 3040 TP1
C / Concrete structure
At least one facade accessible by a firetruck from the ground
A
B
C

## Slide 35
Technical details

## Slide 36
Technical detail : North - South cross section through a dwelling and connexion to the ceiling
Partition wall
Layer build-up A in cm
1.3 Interior plaster
1.3 Interior plaster
5.0 ISOVER Akustic TP 1
1.3 Interior plaster
1.3 Interior plaster
Ceiling
Layer build-up B in cm
Floor covering
5.0 Concrete screed with underfloor heating
1.5 Thermal insulation
0.2 ISOVER VARIO KM Duplex
18.0 Concrete ceiling
1.0 interior plaster
8.0 ISOVER Akustic TP 1
2.7 Rigips ceiling profile CD 60/27 as basic profile
2.7 Rigips ceiling profile CD 60/27 as suppor- ting profile
2.5 Rigips RIGIDUR H double layer
Exterior wall
Layer build-up C in cm
1.0 Interior plaster
0.2 ISOVER VARIO KM Duplex
20.0 Concrete
14.0 ISOVER Sillatherm WVP 1-035
14.0 ISOVER Sillatherm WVP 1-035
1.5 Thick plaster
U VALUE : 0.11 W/M2 K
A
B
C

## Slide 37
Technical details : Two types of ground connexion
Patio door / Opaque wall
Wall to unheated parking Layer build-up B in cm
1.3 Interior plaster
0.2 ISOVER VARIO KM Duplex
20.0 Concrete
14.0 ISOVER Sillatherm WVP 1-035
14.0 ISOVER Sillatherm WVP 1-035
1.5 Thick plaster
Floor to ground
Layer build-up A in cm
Floor covering
5.0 Concrete screed
0.2 ISOVER VARIO KM Duplex
3.0 ISOVER Akustic EP 3 040
4.0 ISOVER Exporit EPS 100/035 as compensation for height of tube
0.5 sealing against moisture
30.0 Concrete foundation slab Separating layer
10.0 Styrodur CS
10.0 Styrodur CS
10.0 Styrodur CS
Granular subbase
U VALUE : 0.1 W/m2K
U VALUE : 0.11 W/m2K
A
A
B

## Slide 38
Roof
Layer build-up A in cm
8.0 Pebbles
0.8 Double layer roof and sealing sheeting, bonded or scorched
18.0 ISOVER Metac FLP 1 Duratec
18.0 ISOVER Metac FLP 1 Duratec Vapour retarder
Levelling layer, bitumen perforated glass-mat sheeting
Preliminary coat bonding course
Concrete laid at inclination of at least 2 %
20.0 Reinforced concrete ceiling
0.2 ISOVER VARIO KM Duplex
1.5 Interior plaster
U VALUE : 0.11 W/m2 K
Exterior wall
Layer build-up B in cm
1.0 Interior plaster
0.2 ISOVER VARIO KM Duplex
20.0 Concrete
14.0 ISOVER Sillatherm WVP 1-035
14.0 ISOVER Sillatherm WVP 1-035
1.5 Thick plaster Perforated steel shutter
U VALUE : 0.11 W/m2 K
Technical detail : West facade and its connexion to the roof
A
B
ISOVER DESIGNER v.3.5 calculations
Annual heat demand : 8.47 kWh/m2a

## Slide 39: Baqsh’Astana
Thank you !
Sophie LAMBOTTE Xiang LI