## Slide 1
Efficient Multi-Robot SLAM in a Labyrinth Environment
Final Presentation
ROBT Capstone II
Abdirakhman Onabek
Ramazan Andarbayev
Bayurzhan Askarov
Supervisor: Prof. Zhanat Kappassov
NAZARBAYEV UNIVERSITY
Page 1 of 40

## Slide 2
Overview
  Introduction
  Statement of the Problem
  Review of Related Literature
  Framework
  Hypothesis
  Methodology
  Conclusion
  Execution
  Q&A
  Limitations and Future Work
  References
Page 2 of 40

## Slide 3
Statement of the Problem
Objectives
  Global matching
  Local Matching
  Pose graph optimisation
Whether multiple robots can map a complex environment fast and efficiently, while overcoming the issues of data consistency, map merging, and communication overhead.
Page 3 of 40

## Slide 4
Review of Related Literature
RTAB-Map Framework
  Optimized for environments with large datasets through selective memory management, with sensor choice impacting performance.
C-SLAM (Collaborative SLAM)
  Focuses on pose graph sparsification and loop closure detection with distributed methods, using the Distributed Gauss-Seidel (DGS) for map optimization, reducing reliance on centralized communication.
TSLAM (Team SLAM Framework)
  Centralized system where robots perform local SLAM independently and send data to a central workstation for global optimization.
Page 4 of 40

## Slide 5
Hypothesis
Can it be more efficient?
Should it be collaborative?
Can it be faster?
Multiple Turtlebots are better than one in terms of mapping of complex environments
Page 5 of 40

## Slide 6
Setup | 2 Turtlebots, LIDAR, labyrinth, decentralized communication
Metrics | Mapping time, Accuracy, Map completeness
Procedure 1 | Single-Robot SLAM
Procedure 2 | Independent SLAM of 2 and more robots
Procedure 3 | Pose Graph Optimization
Procedure 4 | Real-life testing and metrics evaluation
Methodology
Page 6 of 40

## Slide 7
Pose graph
Nodes (robot poses)
Edges (node transforms)
Represents the movement and observations of a robot as it explores an environment
Page 7 of 40

## Slide 8
Intra-robot Loop Closure
A robot creates a certain pose graph, and then revisits a noticeable feature. This will create new edges between existing nodes
Loop closure is a 3D point cloud of a noticeable feature that increased graph connectivity
Page 8 of 40

## Slide 9
Turtlebot #1
local map
Turtlebot #2
local map
Gazebo map
Page 9 of 40

## Slide 10
Inter-robot Loop Closure
Page 10 of 40

## Slide 11
Framework
  Centralized collaborative SLAM framework
  Coupling of LIDAR and odometry through gmapping and then C-Slam
Page 11 of 40

## Slide 12
SIngle-robot slam and navigation
Page 12 of 40

## Slide 13
Page 13 of 40

## Slide 14
Two robot slam and map merging
Page 14 of 40

## Slide 15
Page 15 of 40

## Slide 16
Page 16 of 40

## Slide 17
Page 17 of 40

## Slide 18
Page 18 of 40

## Slide 19
Page 19 of 40

## Slide 20
Λ2​ = 0.27
Λ2​ = 0.41
Graph Sparsification
Page 20 of 40

## Slide 21
Graph Sparsification for Turtlebot 1
Page 21 of 40

## Slide 22
Graph Sparsification for Turtlebot 2
Page 22 of 40

## Slide 23
Page 23 of 40

## Slide 24
Page 24 of 40

## Slide 25
Laplacian Matrix
Λ2​ = 0.72
Page 25 of 40

## Slide 26
Algebraic connectivity maximization
Page 26 of 40

## Slide 27
Page 27 of 40

## Slide 28
Page 28 of 40

## Slide 29
Page 29 of 40

## Slide 30
Bayesian fusion
Page 30 of 40

## Slide 31
Inter-robot loop closure candidates
Page 31 of 40

## Slide 32
The result that we want to get
Page 32 of 40

## Slide 33
Pose graph #1 sparsified
Page 33 of 40

## Slide 34
Pose graph #2 sparsified
Page 34 of 40

## Slide 35
Algebraic connectivity maximization
Page 35 of 40

## Slide 36
Page 36 of 40

## Slide 37
Conclusion
Implementation results
Simulation and real experiments show positive results
Optimized SLAM method
SLAM works too
Map acquiring
We got the map of labyrinth
Page 37 of 40

## Slide 38
Limitations and Future Work
/Onboard computing
  TurtleBots typically have limited computational power compared to high-performance simulation environments.
/Variability
  Differences in lighting, texture, and obstacles can make mapping less predictable than in controlled simulations
/Hardware Constraints
  Real-world sensors (e.g., LIDAR, cameras) may have noise, reduced resolution, or inaccuracies due to environmental factors
/Map merging
  Map merging in real experiments is not done online
Page 38 of 40

## Slide 39
  S. Saeedi, M. Trentini, M. Seto, and H. Li, “Multiple-robot simultaneous localization and mapping: A review,” Journal of Field Robotics, vol. 33, no. 1, pp. 3–46, 2016.
  I. Deutsch, M. Liu, and R. Siegwart, “A framework for multi-robot pose graph slam,” in 2016 IEEE International Conference on Real-time Computing and Robotics (RCAR), pp. 567–572, 2016.
  J. Zhao, S. Liu, and J. Li, “Research and implementation of autonomous navigation for mobile robots based on slam algorithm under ros,” Sensors, vol. 22, no. 11, 2022
  M. Kegeleirs, G. Grisetti, and M. Birattari, “Swarm slam: Challenges and perspectives,” Frontiers in Robotics and AI, vol. 8, 2021.
  M. Labb´e and F. Michaud, “Rtab-map as an open-source lidar and visual simultaneous localization and mapping library for large-scale and long-term online operation,” Journal of Field Robotics, vol. 36, no. 2, pp. 416–446, 2019.
References
  P.-Y. Lajoie and G. Beltrame, “Swarm-slam: Sparse decentralized collaborative simultaneous localization and mapping framework for multi-robot systems,” IEEE Robotics and Automation Letters, vol. 9, p. 475–482, 2024.
Page 39 of 40

## Slide 40
Q&A
Thank you for listening!
Page 40 of 40