## Slide 1: MCH “Gemini”
Architectural Form Follows
for the Climate.
Charles Correa

## Slide 2: 5 external factors :
Air
Water
Earth
Sun
Greenery

## Slide 3: Conception
Kazakh native ornament as a source for site plan idea
Building form a silhouette that creates an imitation of complicated terrain
Different floor levels (East architecture principles)
Climate wall

## Slide 4: Wind protection
Supporting walls with compound configuration
Green wind protecting lanes with strong winds path correction
Landscape channels, walls
Special streamlined building configuration

## Slide 5: Thermal insulation
Climate wall (A spaces between it and living area works like a vestibule)
Streamlined form
Full absence of cold bridges
Isover materials

## Slide 6: Soundproofing
Triple glazing
Climate wall
Floating floors
Green plantings as a noise reflector
noise
wind

## Slide 7: Air quality
Recuperation
Air updrafts as natural ventilation

## Slide 8: Fire protection
Exterior fire ladders
Interior ladders with fire protection spaces

## Slide 9: Insolation
Placement of the building to the cardinal
Enough number of window glazing
Heat protection (visors)
N

## Slide 10: Alternative energy sources
Geothermal energy
Vertical windmills on the roof and built in construction windmills

## Slide 11: Gallery house

## Slide 12: Section house

## Slide 13: Materials used
Isover OL-E (walls against air)
Isover Extra (walls against ground, roof)
Isover floating floors
Isover noise reduction
Isover vario (bathroom ceiling)

## Slide 14: Results
Gallery house Section house
15.01 kWh/(m2a)
10.85 kWh/(m2a)

## Slide 15: Expo 2017 – «Gemini»

## Slide 20: Thank you for attention!